## Slide 1: BASICS OF RC PLANE

## Slide 2: Overview
What is RC Plane?
RC Planes’ Parts and their Role
How planes fly?
Concepts and Terminologies of RC Plane
Stability and Control
How to design your own plane?
Building your own design
How to fly?

## Slide 3: What is RC Plane?
Small radio-controlled model airplanes powered using electric motor or gas engines
Flown using transmitter with joysticks

## Slide 4: Different Parts of RC Plane
Cockpit
Jet Engine
Wing
Horizontal Stabiliser
Vertical Stabiliser
Rudder
Elevator
Flaps
Ailerons
Spoilers
Slats
Fuselage (Body)

## Slide 5: Different Parts of RC Plane

## Slide 6: Different Parts of RC Plane
We can categorize different parts of RC plane as following:
Control Surfaces which are ailerons, elevators and rudder.
Stabilizers include vertical and horizontal stabilizer.
Other parts which include fuselage, engine or power source and propeller.

## Slide 7: Different Parts of RC Plane

## Slide 8: Forces on Plane
The negative forces:-
  Drag
  Weight
We counter them by:-
  Lift for Weight
  Thrust for Drag

## Slide 9: How the planes fly?
Lift Generation
What is Lift?
Airfoil?
Angle of Attack?
L = ½ ρV2AαCL
CL ~ 0.8-1

## Slide 10: Concepts and Terminologies
Drag

## Slide 11: Concepts and Terminologies
  Thrust

## Slide 12: Summing Up

## Slide 13: Concepts and Terminologies
Angle of attack

## Slide 14: Concepts and Terminologies
Wing Chord (c)
Wing Span (b)
Plane form Area (s)
Aspect Ratio (AR)

## Slide 15: Concepts and Terminologies
Effect of Aspect Ratio on Lift

## Slide 16: Concepts and Terminologies
Effect of Aspect Ratio on Drag

## Slide 17: Stability and Control
A plane can rotate about three axes-
  Roll
  Pitch
  Yaw
To attain control over these three axes, we have-
  Ailerons for Roll
  Elevator for Pitch
  Rudder for Yaw

## Slide 18: Stability and Control
Roll Motion

## Slide 19: Roll Motion

## Slide 20: Concepts of RC Plane
Pitch Motion

## Slide 21: Pitch Motion

## Slide 22: Stability and Control
Horizontal Stabilizer

## Slide 23: Stability and Control
Yaw Motion

## Slide 24: Yaw Motion

## Slide 25: Axes of Rotation

## Slide 26: How to make your own?
Step 1
Developing your own design
Step 2
Constructing your own design
Step 3
How to fly?

## Slide 27
Determine wing dimensions
  Set lift = target aircraft weight
  Use approximate velocity to determine the area
                CL ~ 0.8 - 1
                ρ = Density of air (1.225)
                V = velocity of the aircraft
                S = Wing area
  Select A.R (4 – 6). Determine chord and wingspan
Step 1
Developing your own Design

## Slide 28
Determine wing dimensions
Horizontal Tail Sizing
  H.T.A ~ 20% of wing area
  H.T.A = Horizontal Tail Area
  Horiz. Tail at approx. 2.5 times to the aft of CG
  A.R to lie in the range of 4-5
Step 1
Developing your own Design

## Slide 29
Determine wing dimensions
Horizontal Tail Sizing
Vertical Tail Sizing
  V.T.A = 8 – 10% of Wing area
  V.T.A = Vertical Tail Area
  Aspect Ratio in the range of 2.5-3
Step 1
Developing your own Design

## Slide 30
Determine Wing dimensions
Horizontal Tail Sizing
Vertical Tail Sizing
Determining fuselage length
  Fuselage length ~ 0.8 times wingspan
  Fuselage length from CG to Horizontal Stabilizers ~2.5 times wing chord
Step 1
Developing your own Design

## Slide 31
Determine Wing dimensions
Horizontal Tail Sizing
Vertical Tail Sizing
Determining fuselage length
CG location
  CG should be ahead of the wing’s quarter chord
Step 1
Developing your own Design

## Slide 32
Determine Wing dimensions
Horizontal Tail Sizing
Vertical Tail Sizing
Determining fuselage length
CG location
Wing Positioning
  High wing configuration
    Easy to construct and stable
Step 1
Developing your own Design

## Slide 33
Determine Wing dimensions
Horizontal Tail Sizing
Vertical Tail Sizing
Determining fuselage length
CG location
Wing Positioning
Electronic Component Selection
Step 1
Developing your own Design

## Slide 34: Electronic Component Selection
Powerplant
  BLDC (Brushless DC Motor)
  Propeller
  ESC (Electronic Speed Controller )
Servo Motors
Li-Po Battery
Transmitter & Receiver
We will go over them in the upcoming sessions

## Slide 35: Brushless DC Motor Electronic Speed Controller
Servo Motor

## Slide 36: Li – Po Battery
Propeller

## Slide 37: Safety Regarding Li-Po
Never Discharge LiPo Completely
Always Store in Cool Location away from sunlight
Away from flammable materials
Always wrap in foam for crash resistance
Use appropriate connectors (Ultra Deans)
Never discharge over C limit(30C burst-30sec)
Next Lipo-Explosion

## Slide 38
Materials required for the structure
  Styrofoam
  Corrugated Plastic (Coroplast)
  Balsa Wood
Step 2
Constructing your own Design
Other materials required for constructing
  Epoxy Glue (Bond – Tite)
  Masking Tape
  Double – Sided Tape (DST)
  Cutters
  We will further discuss about the materials to choose in the upcoming sessions.

## Slide 39: Styrofoam Coroplast
Balsa wood

## Slide 40: Bond – Tite (Epoxy Glue) Double – Sided Tape (DST)
Masking Tape Cutter

## Slide 41
Points to note
Symmetric construction
  Make sure the plane is symmetrical about roll axis
  CG should ideally lie on the roll axis
Keep the CG as low as possible
Keep the empennage (horizontal wing and vertical wing together) light
Step 2
Constructing your own Design

## Slide 42
Get comfortable with the controls.
How to Fly?
Step 3

## Slide 43
Proper Practice!
One Stop Solution for the above is SIMULATOR SESSION.
Be ready for Crash :P
How to Fly?
Step 3

## Slide 44: What Next?
Decide your team (max. 4 and min. 2)
Register your team (Also a Good name :P)
Registration link on
  STAB website
  FB Group
  Google Group
Allotment of Mentors
Then It’s all about your enthu and efforts. :D
Where is your effort required?
  Attending workshops
  Simulator practice Sessions
  Flying practice Sessions

## Slide 45: THANK YOU!!!